## Slide 1
General License Class
Lesson 3
Digital Modes

## Slide 2
Introduction to Digital Modes
Exchange digital data via radio between two computing systems.
  E-mail, files, keyboard-to-keyboard, messages, etc.
New modes being developed all the time.
More and more amateurs are using digital modes.

## Slide 3
Where to Find Digital Activity
  Restricted to CW/data segments of each band.
  Usually close to the top end of the CW segment, but check the band plan.
    160m -- bottom end of band.
    60m – center of each channel.
    10m – middle of CW segment.
Introduction to Digital Modes

## Slide 4
Band | Digital Mode Frequencies
160m | 1.800 MHz to 1.810 MHz
80m | 3.570 MHz to 3.600 MHz
60m | Center of each channel.
40m | 7.035 MHz to 7.045 MHz (ITU Regions 1 & 3) 7.080 MHz to 7.125 MHz (ITU Region 2)
20m | 14.070 MHz to 14.0995 MHz (14.070 MHz = PSK31) 14.1005 MHz to 14.112 MHz
17m | 18.100 MHz to 18.110 MHz
15m | 21.070 MHz to 21.110 MHz
12m | 24.920 MHz to 24.930 MHz
10m | 28.070 MHz to 28.150 MHz
Introduction to Digital Modes

## Slide 5
Digital Voice & Image Modes
  Digital voice systems are considered voice modes by the FCC.
    FreeDV, D-Star, SystemFusion, WinDRM, etc.
    Operations in voice/image sections of the band.
  SSTV operations are converting from current analog systems to digital file transfers, but still considered image mode.
Introduction to Digital Modes

## Slide 6
Digital Mode Overview
  Communicating by encoding characters as combinations of bits.
  Consists of a protocol and a method of modulation.
    Protocol – Rules for encoding the data.
Introduction to Digital Modes

## Slide 7
Digital Mode Overview
  Maximum data rates determined by FCC regulations.
    FCC considering changing to bandwidth limits.
  If you create your own digital code, you must make the protocol rules public.
Introduction to Digital Modes

## Slide 8
Radioteletype (RTTY).
  Oldest digital mode.
  Adapted from land-line teletype system.
    Frequency shift keying (FSK).
    Audio frequency shift keying (AFSK).
  5-bit Baudot code.
    Letters A-Z.
      No lower case.
    Numbers 0-9.
    Some punctuation.
Introduction to Digital Modes

## Slide 9
PSK31.
  Phase shift keying.
  31.25 baud.
  Narrowest bandwidth of any mode, including CW.
  Very effective in noisy conditions.
Introduction to Digital Modes

## Slide 10
PACTOR
  Developed by Special Communications Systems GmBH.
  PACTOR I.
    Open technology  Relatively inexpensive modems.
      $50.00 to $150.00.
  PACTOR II, PACTOR III, & PACTOR IV.
    Proprietary technology  Very expensive modems.
      $1000.00 to >$1600.00.
  Used in NTS digital message handling system.
Introduction to Digital Modes

## Slide 11
WINMOR & Winlink
  WINMOR = Windows Messaging Over Radio
    Ability to detect and correct errors.
  Winlink
    Uses gateways to connect to internet for passing messages.
    Radio-based e-mail.
Introduction to Digital Modes

## Slide 12
Packet.
  Oldest of “modern” digital modes.
    Became widely popular in 1980’s.
    Still popular on VHF.
      1200-9600 baud on 2m.
    Not practical on HF.
      Limited to 300 baud.
      Very slow when band is busy or conditions are noisy.
Introduction to Digital Modes

## Slide 13
Amateur Digital Modes.
  Olivia.
    Variation of MFSK.
    Very effective at poor signal-to-noise levels.
      S/N = -14 dB.
    Relatively slow but robust.
Introduction to Digital Modes

## Slide 14
Amateur Digital Modes.
  MFSK.
    Multi-tone frequency shift keying.
    Forward error correction (FEC).
      Extra information sent to allow reconstruction of original data in the presence of data.
Introduction to Digital Modes

## Slide 15
Digital Modes
  Miscellaneous Digital Modes
    WSJT and JT44/JT65
      Designed for VHF/UHF meteor scatter and moonbounce communications.
      Adapted for HF
      Can decode signals below noise level.
Introduction to Digital Modes

## Slide 16
Miscellaneous Digital Modes
  Hellscreiber
    Used for sending images encoded as digital data.
  JT65 & JT9
    Variations of WSJT family of modes.
    Can decode weak signals in presence of noise.
  WSPR (Whisper)
    Very low signal-to-noise ratios.
Introduction to Digital Modes

## Slide 17
Digital Basics
Errors in Digital Modes.
  Error Correction.
    Forward Error Correction (FEC).
      Adds extra information so that data can be reconstructed.
        e.g. - MFSK-16
    Automatic Repeat Request (ARQ).
      If error detected, asks sending station to retransmit data.
        e.g. – Packet, WINMOR

## Slide 18
G2E04 -- What segment of the 20-meter band is most often used for digital transmissions?
A. 14.000 - 14.050 MHz
B. 14.070 - 14.100 MHz
C. 14.150 - 14.225 MHz
D. 14.275 - 14.350 MHz

## Slide 19
G2E07 -- What segment of the 80-meter band is most commonly used for digital transmissions?
A. 3570 – 3600 kHz
B. 3500 – 3525 kHz
C. 3700 – 3750 kHz
D. 3775 – 3825 kHz

## Slide 20
G2E08 -- In what segment of the 20 meter band are most PSK31 operations commonly found?
A. At the bottom of the slow-scan TV segment, near 14.230 MHz
B. At the top of the SSB phone segment near 14.325 MHz
C. In the middle of the CW segment, near 14.100 MHz
D. Below the RTTY segment, near 14.070 MHz

## Slide 21
G2E13 -- Which communication system sometimes uses the Internet to transfer messages?
A. Winlink
B. RTTY
C. ARES
D. Skywarn

## Slide 22
G8C01 -- Which of the following digital modes is designed to operate at extremely low signal strength on the HF bands?
A. FSK441 and Hellschreiber
B. JT9 and JT65
C. Clover
D. RTTY

## Slide 23
Digital Basics
Definitions
  Mode.
    Amateur transceivers designed for voice transmission can be used to send digital information (data) as a series of tones.
    Data modes consist of:
      Modulation method.
        How tones are added to RF signal.
      Protocol.
        Rules governing how data is converted to tones.

## Slide 24
Definitions
  Bit Rate vs. Baud.
    Bit Rate = Number of bits per second.
    Baud = Number of symbols per second.
      Symbol = signal characteristic(s) that make up a distinct state of transmitted signal.
    In simple codes, 1 symbol = 1 bit, & bit rate = baud.
      ASCII, Baudot, etc.
    In more complex codes, 1 symbol may encode more than one bit, & bit rate > baud.
Digital Basics

## Slide 25
Frequency Shift Keying (FSK)
  Individual data bits represented by two or more discreet frequencies.
    Older modes use 2 frequencies.
      Frequencies called “mark” & “space”.
      RTTY, Packet, etc.
    New modes use more than 2 frequencies.
      Olivia, MFSK-16, MFSK-32, etc.
      16 or 32 most common on HF.
      128 & 256 being used by VOA to send images.
      MFSK32 uses 32 frequencies.
Digital Basics

## Slide 26
Frequency Shift Keying (FSK)
  FSK – In true FSK, the data bits are applied directly to transmitter VFO to shift the carrier frequency.
    a.k.a. – Direct FSK.
    Only possible for modes where only one tone sent at a time.
  AFSK – Data bits are converted to tones used to modulate an SSB or FM transmitter.
    Convenient.
    Can be used with any digital mode.
Digital Basics

## Slide 27
Phase Shift Keying (PSK)
  Individual data bits represented by phase shifts in signal.
    Most common type is inversion (180° phase shift).
    Phase shift can be referenced to same signal at earlier point in time or to another tone.
    Sounds like raspy buzz or noise.
    PSK31, etc.
Digital Basics

## Slide 28
G8A01 -- How is an FSK signal generated?
A. By keying an FM transmitter with a sub-audible tone
B. By changing an oscillator’s frequency directly with a digital control signal
C. By using a transceiver’s computer data interface protocol to change frequencies
D. By reconfiguring the CW keying input to act as a tone generator

## Slide 29
G8C11 -- How are the two separate frequencies of a Frequency Shift Keyed (FSK) signal identified?
A. Dot and Dash
B. On and Off
C. High and Low
D. Mark and Space

## Slide 30
Character-Based Modes
The simplest form of digital communications is where the operator enters a character & that character is transmitted to the receiving station.
  a.k.a. – Keyboard-to-keyboard communications.
    CW
    RTTY
    PSK31

## Slide 31
Radioteletype (RTTY).
  Baudot code.
    Start bit, 5 data bits, & stop bit.
    A-Z, 0-9, CR, LF, LTRS, FIGS, punctuation, & control codes.
Character-Based Modes

## Slide 32
Radioteletype (RTTY).
  Standard tones:
    2125 Hz (mark)
    2295 Hz (space).
    Shift = 170 Hz.
  Standard speeds:
    60 wpm (45 baud) – Most common
    75 wpm (56 baud
    100 wpm (75 baud).
Character-Based Modes

## Slide 33
Multiple Frequency Shift Keying (MFSK).
  Uses more than 2 tones to encode the data.
Mode | Number of Tones | Bandwidth
MFSK-32 | 32 | 500 Hz
MFSK-32 | 64 | 1 kHz
MT63-1KL | 64 | 1 kHz
MT63-2KL | 64 | 2 kHz
Olivia | 4 to 64 | 250 Hz to 2 kHz
Character-Based Modes

## Slide 34
PSK31.
  Most popular phase-shift keying mode.
  Single-tone.
  Symbol is phase reversal of tone.
    Symbol rate (baud) = 31.25
  Variable length code (Varicode).
    Shorter codes for more common characters.
    Upper case letters have longer codes than lower case.
  PSK63 (symbol rate = 63) becoming popular.
Character-Based Modes

## Slide 35
G2E06 -- What is the most common frequency shift for RTTY emissions in the amateur HF bands?
A. 85 Hz
B. 170 Hz
C. 425 Hz
D. 850 Hz

## Slide 36
G8C02 -- How many data bits are sent in a single PSK31 character?
A. The number varies
B. 5
C. 7
D. 8

## Slide 37
G8C04 -- Which of the following describes Baudot code?
A. A 7-bit code with start, stop and parity bits
B. A code using error detection and correction
C. A 5-bit code with additional start and stop bits
D. A code using SELCAL and LISTEN

## Slide 38
G8C08 -- Which of the following statements is true about PSK31?
A. Upper case letters make the signal stronger
B. Upper case letters use longer Varicode signals and thus slow down transmission
C. Varicode Error Correction is used to ensure accurate message reception
D. Higher power is needed as compared to RTTY for similar error rates

## Slide 39
G8C09 -- What does the number 31 represent in "PSK31"?
A. The approximate transmitted symbol rate
B. The version of the PSK protocol
C. The year in which PSK31 was invented
D. The number of characters that can be represented by PSK31

## Slide 40
G8C12 -- Which type of code is used for sending characters in a PSK31 signal?
A. Varicode
B. Viterbi
C. Volumetric
D. Binary

## Slide 41
Packet-Based Modes
Packet-based or structured modes are derived form early computer-to-computer (internet) data transfer protocols.
  Amateurs modified these protocols to develop Packet, PACTOR, WINMOR, & other communications systems.

## Slide 42
Packet Basics.
  Packet transmission means that the data is divided up into “chunks” & transmitted a “chunk” at a time.
  Additional data is added to each “chunk” to facilitate the transfer of the data.
  Each chunk along with the additional data is called a “packet”.
Packet-Based Modes

## Slide 43
Packet Basics.
  All packet-based systems have the same basic structure for the packets:
    Header – Placed before the data & contains bit patterns to synchronize the receiver, control & routing information, and sometimes error detection/correction information.
    Data – The data being sent, usually ASCII characters.
    Trailer – Additional control & status information, and information used for error detection.
Packet-Based Modes

## Slide 44
Packet Basics.
  The process of encapsulating data into a packet allows for error detection.
    Cyclic Redundancy Check (CRC) – Data in trailer of packet calculated based on all other data in the packet.
    If CRC does not match, then data was not received correctly.
Packet-Based Modes

## Slide 45
Packet Basics.
  Error Detection & Correction.
    Automatic Repeat Request (ARQ) – If CRC or other error detection mechanism fails, then receiving station asks for the packet to be sent again.
      ACK character sent by receiving station when packet was received correctly.
      NAK character sent by receiving station when packet needs to be repeated.
Packet-Based Modes

## Slide 46
Packet Basics.
  Error Detection & Correction.
    Forward Error Correction (FEC) – Additional information is sent with additional data to allow receiving station to correct for some types of error.
Packet-Based Modes

## Slide 47
Packet Basics.
  ARQ systems designed to exchange information between 2 stations.
    Receiving station has to acknowledge each packet was received correctly.
    Only one station can send the acknowledgement.
    Cannot “break in” to QSO between stations using ARQ.
    Other stations can use monitor mode (MON) to “listen in” without having the benefits of error detection.
Packet-Based Modes

## Slide 48
Packet Basics.
  ARQ systems provide a “broadcast” or “unconnected” mode so that a station can announce its presence (call “CQ”).
    APRS consists entirely of unconnected packets.
Packet-Based Modes

## Slide 49
Packet Radio.
  Used almost exclusively on VHF or UHF FM.
    1200 or 9600 baud.
  Based on the internet X.25 protocol.
    AX.25 protocol.
  Not suitable for HF.
    Limited to 300 baud by FCC.
    Errors due to noise & fading result in numerous repeat requests .
Packet-Based Modes

## Slide 50
PACTOR and WINMOR.
  No error detection/correction possible with RTTY.
  Teletype-over-radio (TOR) modes developed to overcome this shortcoming.
Packet-Based Modes

## Slide 51
PACTOR and WINMOR.
  PACTOR
    Packet-based.
    PACTOR-I uses FSK.
    PACTOR-II, PACTOR-III, & PACTOR-4 use PSK.
      PACTOR-4 not legal for amateur use in US.
  WINMOR
    Uses either FSK or PSK.
Packet-Based Modes

## Slide 52
PACTOR and WINMOR.
  Both use ARQ for error detection/correction.
  Preferred methods for transferring large amounts of data over amateur radio.
  Preferred methods of transmission for WinLink.
Packet-Based Modes

## Slide 53
G2E02 -- How can a PACTOR modem or controller be used to determine if the channel is in use by other PACTOR stations?
A. Unplug the data connector temporarily and see if the channel-busy indication is turned off
B. Put the modem or controller in a mode which allows monitoring communications without a connection
C. Transmit UI packets several times and wait to see if there is a response from another PACTOR station
D. Send the message: "Is this frequency in use?"

## Slide 54
G2E09 -- How do you join a contact between two stations using the PACTOR protocol?
A. Send broadcast packets containing your call sign while in MONITOR mode
B. Transmit a steady carrier until the PACTOR protocol times out and disconnects
C. Joining an existing contact is not possible, PACTOR connections are limited to two stations
D. Send a NAK response continuously so that the sending station has to pause

## Slide 55
G8C03 -- What part of a data packet contains the routing and handling information?
A. Directory
B. Preamble
C. Header
D. Footer

## Slide 56
G8C05 -- In the PACTOR protocol, what is meant by an NAK response to a transmitted packet?
A. The receiver is requesting the packet be retransmitted
B. The receiver is reporting the packet was received without error
C. The receiver is busy decoding the packet
D. The entire file has been received correctly

## Slide 57
G8C07 -- How does the receiving station respond to an ARQ data mode packet containing errors?
A. It terminates the contact
B. It requests the packet be retransmitted
C. It sends the packet back to the transmitting station
D. It requests a change in transmitting protocol

## Slide 58
G8C10 -- How does forward error correction (FEC) allow the receiver to correct errors in received data packets?
A. By controlling transmitter output power for optimum signal strength
B. By using the varicode character set
C. By transmitting redundant information with the data
D. By using a parity bit with each character

## Slide 59
Receiving and Transmitting Digital Modes
All digital modes except for RTTY are transmitted as USB signals.
  When RTTY is sent using AFSK, it is transmitted as a LSB signal.
NOTE: The book is wrong!

## Slide 60
Bandwidth of Digital Modes.
  The FCC defines the bandwidth of digital signals the same as for any other mode.
  Bandwidth depends on symbol rate.
    Higher symbol rate  Wider bandwidth.
    Some protocols can adjust symbol rate & bandwidth during a contact as conditions change.
Receiving and Transmitting Digital Modes

## Slide 61
Bandwidth of Digital Modes.
Mode | Bandwidth
PSK31 | 50 Hz
RTTY | 200 Hz
MFSK16 | 300 Hz
JT65 | 350 Hz
DominoEX | 524 Hz
Mode | Bandwidth
Olivia | 1000 Hz
WINMOR | 1600
MT63 | 2000 Hz
PACTOR-III | 2300 Hz
PACTOR-4 | 2300 Hz
Receiving and Transmitting Digital Modes

## Slide 62
Bandwidth of Digital Modes.
  Be aware of the band edges!
    If running RTTY using AFSK, keep the VFO frequency at least 2.3 kHz above the lower limit of the data segment or band.
    For other modes, keep VFO frequency below the lower limit of the data segment or band by an amount greater than the highest frequency being transmitted.
      > fC + 0.5fBW
Receiving and Transmitting Digital Modes

## Slide 63
Transmitter Duty Cycle.
  Average power output of a transmitter depends on the duty cycle of the mode.
    CW ≈ 40%
    SSB ≈ 25-40%
    AM ≈ 50%
    FM = 100%
    RTTY & Digital = 100%
Receiving and Transmitting Digital Modes

## Slide 64
Transmitter Duty Cycle.
  Most HF amateur transceivers are rated for Intermittent Commercial and Amateur Service (ICAS).
    Cannot run at full power output for long transmissions without overheating.
    Should reduce output power to about 50% of rated output when operating RTTY or other digital modes to prevent damage.
Receiving and Transmitting Digital Modes

## Slide 65
Digital Mode Signal Quality.
  Same concerns as with SSB or CW for interfering with other nearby QSO’s.
  Too much signal from soundcard to transmitter microphone input causes distortion.
    Splatter & other spurious emissions.
    Receiving station cannot decode signal.
    Shows up as additional lines on receiving station’s waterfall display.
Receiving and Transmitting Digital Modes

## Slide 66
ALC and Digital Modes.
  By design, ALC distorts signal to avoid excessive power output.
    Added distortion acceptable compromise for voice.
    Added distortion not acceptable for digital signals.
      Signals are difficult to decode.
      Generates spurious signals.
  Disable ALC or lower microphone gain so that ALC never activates.
Receiving and Transmitting Digital Modes

## Slide 67
G2E01 -- Which mode is normally used when sending an RTTY signal via AFSK with an SSB transmitter?
A. USB
B. DSB
C. CW
D. LSB

## Slide 68
G2E05 -- What is the standard sideband used to generate a JT65 or JT9 digital signal when using AFSK in any amateur band?
A. LSB
B. USB
C. DSB
D. SSB

## Slide 69
G2E11 -- What is indicated on a waterfall display by one or more vertical lines adjacent to a PSK31 signal?
A. Long Path propagation
B. Backscatter propagation
C. Insufficient modulation
D. Overmodulation

## Slide 70
G2E14 -- What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly?
A. The mark and space frequencies may be reversed
B. You may have selected the wrong baud rate
C. You may be listening on the wrong sideband
D. All of these choices are correct

## Slide 71
G4A14 -- What is likely to happen if a transceiver’s ALC system is not set properly when transmitting AFSK signals with the radio using single sideband mode?
A. ALC will invert the modulation of the AFSK mode
B. Improper action of ALC distorts the signal and can cause spurious emissions
C. When using digital modes, too much ALC activity can cause the transmitter to overheat
D. All of these choices are correct

## Slide 72
G8B05 -- What is the approximate bandwidth of a PACTOR3 signal at maximum data rate?
A. 31.5 Hz
B. 500 Hz
C. 1800 Hz
D. 2300 Hz

## Slide 73
G8B08 -- Why is it important to know the duty cycle of the mode you are using when transmitting?
A. To aid in tuning your transmitter
B. Some modes have high duty cycles which could exceed the transmitter's average power rating
C. To allow time for the other station to break in during a transmission
D. All of these choices are correct

## Slide 74
G8B10 -- What is the relationship between transmitted symbol rate and bandwidth?
A. Symbol rate and bandwidth are not related
B. Higher symbol rates require wider bandwidth
C. Lower symbol rates require wider bandwidth
D. Bandwidth is always half the symbol rate

## Slide 75
Digital Operating Procedures
Listen First.
  Just like all other modes, listen first to make certain the frequency is clear.
    Look for signals on waterfall.

## Slide 76
Initiating and Terminating Digital Contacts.
  Essentially same as for CW contacts.
  Calling CQ:
    CQ CQ CQ de K9DUR K9DUR K9DUR
CQ CQ CQ de K9DUR K9DUR K9DUR k
  Answering a CQ:
    W9GWC W9CWC de K9DUR K9DUR K9DUR k
Digital Operating Procedures

## Slide 77
Initiating and Terminating Digital Contacts.
  Digital mode QSO’s use same procedures, prosigns, & Q-signals as CW contacts.
Digital Operating Procedures

## Slide 78
Initiating and Terminating Digital Contacts.
  Some digital modes are “connected” modes.
    Packet, PACTOR, WINMOR, etc.
    Specific “connect” message sent to establish connection between 2 stations.
    Specific “disconnect” message sent to end contact & close connection.
      Connection may be closed automatically if excessive transmission attempts or timeout occurs.
Digital Operating Procedures

## Slide 79
Initiating and Terminating Digital Contacts.
  Gateway and mailbox stations.
    An automatic message-handling system has been established to pass messages from origin to destination by automatic relay.
      A gateway station transfers messages to or from the internet.
      A mailbox station stores messages for pick up by the recipients at a later time.
Digital Operating Procedures

## Slide 80
Initiating and Terminating Digital Contacts.
  Gateway and mailbox stations.
    Some digital messaging stations are unmanned & operate under automatic control.
      In the US, automatically-controlled digital stations are restricted to certain band segments on frequencies below 220 MHz.
      Your station may communicate with an automatically-controlled non-US station operating outside of the specified band segments, but your station must be under local or remote control.
Digital Operating Procedures

## Slide 81
Band | Segment
80m | 3.585 MHz – 3.600 MHz
40m | 7.100 MHz – 7.105 MHz
30m | 10.140 MHz – 10.150 MHz
20m | 14.0950 MHz – 14.0995 MHz 14.1005 MHz – 14.1120 MHz
17m | 18.105 MHz – 18.110 MHz
15m | 21.090 MHz – 21.100 MHz
12m | 24.925 MHz – 24.930 MHz
10m | 28.120 MHz – 28.189 MHz
6m | 50.1 MHz – 50.4 MHz
2m | 144.1 MHz to 148 MHz
Digital Operating Procedures

## Slide 82
Initiating and Terminating Digital Contacts.
  Gateway and mailbox stations.
    Contacts with automatically-controlled stations are initiated by sending a “CONNECT” message.
    Once connection is established, message may be transmitted.
Digital Operating Procedures

## Slide 83
During the Contact.
  Operating Displays.
    Almost all digital mode software programs provide a type of display know as a “waterfall”.
      A portion of the received RF spectrum is displayed as a horizontal line. The color and/or brightness of the line indicates the signal strength.
      As each line is drawn, the previous line(s) are pushed down on the screen & the new line added at the top, giving the impression of a waterfall as the signals flow from top to bottom in the display.
Digital Operating Procedures

## Slide 84
During the Contact.
  Waterfall Display
Digital Operating Procedures

## Slide 85
During the Contact.
  Operating Displays.
    A more accurate display for RTTY signals is the “crossed ellipse” display.
      Many software programs provide the crossed-ellipse display in addition to the normal waterfall display.
        Sometimes called “scope” (short for oscilloscope).
      When the two ellipses are at right angles to each other (vertical & horizontal) then signal is properly tuned in.
        Size of ellipses indicates signal strength.
        Unequal sizes indicates selective fading is occurring.
Digital Operating Procedures

## Slide 86
During the Contact.
  RTTY Display
Digital Operating Procedures

## Slide 87
During the Contact.
  Third-Party Traffic.
    Same rules apply to digital messages as for voice or CW.
      International messages only if third-party agreement exists.
    Use of gateways must be carefully limited.
Digital Operating Procedures

## Slide 88
During the Contact.
  Interfering Signals.
    Like voice or CW signals, digital signals are subject to interference.
      Human brain can recover CW or voice signals in presence of interference.
      Digital software may not be able to decode the desired signal.
    When using keyboard-to-keyboard modes, user may be able to “fill in the blanks” in the received signal.
Digital Operating Procedures

## Slide 89
During the Contact.
  Interfering Signals.
    When using connected modes, signal must get through in its entirety or transmission fails.
      Cannot establish a connection.
      Frequent retries with resulting delays.
      Timeouts or dropped connections.
Digital Operating Procedures

## Slide 90
G1E03 -- What is required to conduct communications with a digital station operating under automatic control outside the automatic control band segments?
A. The station initiating the contact must be under local or remote control
B. The interrogating transmission must be made by another automatically controlled station
C. No third party traffic maybe be transmitted
D. The control operator of the interrogating station must hold an Extra Class license

## Slide 91
G1E11 -- Which of the following is the FCC term for an unattended digital station that transfers messages to and from the Internet?
A. Locally controlled station
B. Robotically controlled station
C. Automatically controlled digital station
D. Fail-safe digital station

## Slide 92
G1E12 -- Under what circumstances are messages that are sent via digital modes exempt from Part 97 third party rules that apply to other modes of communication?
A. Under no circumstances
B. When messages are encrypted
C. When messages are not encrypted
D. When under automatic control

## Slide 93
G1E13 -- On what bands may automatically controlled stations transmitting RTTY or data emissions communicate with other automatically controlled digital stations?
A. On any band segment where digital operation is permitted
B. Anywhere in the non-phone segments of the 10-meter or shorter wavelength bands
C. Only in the non-phone Extra Class segments of the bands
D. Anywhere in the 1.25-meter or shorter wavelength bands, and in specified segments of the 80-meter through 2-meter bands

## Slide 94
G2E03 -- What symptoms may result from other signals interfering with a PACTOR or WINMOR transmission?
A. Frequent retries or timeouts
B. Long pauses in message transmission
C. Failure to establish a connection between stations
D. All of these choices are correct

## Slide 95
G2E10 -- Which of the following is a way to establish contact with a digital messaging system gateway station?
A. Send an email to the system control operator
B. Send QRL in Morse code
C. Respond when the station broadcasts its SSID
D. Transmit a connect message on the station’s published frequency

## Slide 96
G2E12 -- Which of the following describes a waterfall display?
A. Frequency is horizontal, signal strength is vertical, time is intensity
B. Frequency is vertical, signal strength is intensity, time is horizontal
C. Frequency is horizontal, signal strength is intensity, time is vertical
D. Frequency is vertical, signal strength is horizontal, time is intensity

## Slide 97
G8C06 -- What action results from a failure to exchange information due to excessive transmission attempts when using PACTOR or WINMOR?
A. The checksum overflows
B. The connection is dropped
C. Packets will be routed incorrectly
D. Encoding reverts to the default character set