## Slide 1
General License Class
Lesson 2
Procedures &
Practices
Notes: <number>

## Slide 2
HF Operating Techniques
Basic Operating
  HF bands (except 60m) not channelized.
    Equipment designed for continuous tuning
    VFO = Variable Frequency Oscillator

## Slide 3
Basic Operating
  Making a Contact
    CQ – General call to any station
      Restricted CQ’s
        By location -- CQ DX, CQ Europe, CQ Texas, etc.
        Other – CQ Contest, CQ Field Day, etc.
HF Operating Techniques

## Slide 4
Basic Operating
  Making a Contact
    Calling CQ on phone:
CQ CQ CQ this is <your call> <your call> <your call>
CQ CQ CQ this is <your call> <your call> <your call>
CQ CQ CQ this is <your call> <your call> <your call> over
      Use the ICAO phonetic alphabet to send your call.
    Calling CQ on CW:
CQ CQ CQ DE <your call> <your call> <your call>
CQ CQ CQ DE <your call> <your call> <your call>
CQ CQ CQ DE <your call> <your call> <your call> K
HF Operating Techniques

## Slide 5
Basic Operating
  Making a Contact.
    Answering a CQ on phone:
<his call> this is <your call> <your call> <your call> over
      Send <your call> phonetically using ICAO phonetic alphabet.
    Answering a CQ on CW:
<his call> this is <your call> <your call> <your call> K
    Breaking into an existing conversation:
      Send <your call> phonetically during a break between transmissions.
      KN
HF Operating Techniques

## Slide 6
Good Practices
  Selecting a Frequency
      Be aware of the band edges!
HF Operating Techniques

## Slide 7
Good Practices
  Selecting a Frequency
    Signal Separation
Mode | Separation
CW | 150-500 Hz
SSB | Approx 3 kHz
RTTY | 250-500 Hz
PSK31 | 150-500 Hz
HF Operating Techniques

## Slide 8
Good Practices
  Selecting a Frequency
    No single operator or group of operators has priority on a given frequency.
    If a conflict arises, move to a different frequency.
      Change in propagation causes conflict.
      Schedules or nets.
      Courtesy Rules!
HF Operating Techniques

## Slide 9
Good Practices
  Selecting a Frequency
    In Summary:
      Be sure frequency is authorized to General class licensees.
        Be aware of the band edges!
      Follow the band plan, if possible.
      Listen before transmitting!
HF Operating Techniques

## Slide 10
Good Practices
  Nets & Schedules
    Nets – Regularly scheduled gatherings of amateur radio operators on the air for a specific purpose.
      Traffic Nets
      Service Nets
      Social Nets
      Topical Nets
        Every topic you can think of & a few you can’t!
      Emergency Nets
        Obviously, not normally scheduled.
HF Operating Techniques

## Slide 11
Good Practices
  Nets & Schedules
    Schedules – Agreement by 2 or more operators to meet on a specific frequency at a specific time.
HF Operating Techniques

## Slide 12
Good Practices
  Band plans
    Gentlemen’s agreements specifying what segments of a band are used for what mode or type of operation.
    NOT regulations, but guidelines.
      FCC considers band plans to be “good amateur practice” to be followed when practical.
HF Operating Techniques

## Slide 13
Good Practices
  Housekeeping and Operating Support
    Logs
      Not required by FCC, but useful if FCC makes inquiries into station operation.
      Necessary for exchanging QSL cards.
      Necessary for award tracking.
      Necessary for contests.
HF Operating Techniques

## Slide 14
Good Practices
  Housekeeping and Operating Support
    Logs
      Normally contain:
        Date & time of contact.
        Band or frequency of contact.
        Call sign of station worked.
        Signal reports sent/received.
      May contain any other desired information.
        Name & QTH of station contacted, guest operator, etc.
HF Operating Techniques

## Slide 15
Managing Interference
  Types of Interference
    Incidental interference
      Propagation changes
      Not maintaining proper frequency separation
    Harmful interference
      Prohibited by FCC Rules & Regulations
    Malicious (intentional) interference
      Prohibited by FCC Rules & Regulations
HF Operating Techniques

## Slide 16
Managing Interference
  Avoiding Interference
    Be smart.
    Know band conditions.
      Propagation
      Busy times
    Use directional antenna.
HF Operating Techniques

## Slide 17
Managing Interference
  Reacting to Interference
    Change frequency or antenna.
    Have back-up plan.
    Keep cool!!!
HF Operating Techniques

## Slide 18
Modes
  CW
    Continuous wave.
    Best mode for weak-signal conditions.*
    Permitted on ANY amateur frequency.
      Courteous operators stay in segments specified for CW in the band plan.
HF Operating Techniques
Notes: * Some modern digital modes can outperform CW on weak signals.
<number>

## Slide 19
Modes
  AM and SSB Phone
    SSB most common mode on HF.
    SSB narrower bandwidth than AM.
    SSB more power efficient than AM.
    AM higher fidelity than SSB.
HF Operating Techniques

## Slide 20
Modes
  AM and SSB Phone
    SSB – Which sideband?
      60m -- USB only (FCC Regulation)
      On all other bands, sideband is dictated by convention, not by regulation.
HF Operating Techniques

## Slide 21
Band | Sideband
160m | LSB
80m | LSB
40m | LSB
20m | USB
17m | USB
15m | USB
12m | USB
10m | USB
VHF/UHF | USB
Conventional Sideband Usage
HF Operating Techniques

## Slide 22
HF Operating Techniques
Modes
  Digital Modes
    RTTY
    PSK31
    PACTOR
    Olivia
    JT65
    Many, many more!

## Slide 23
HF Operating Techniques
Modes
  Image Modes
    Slow-Scan Television (SSTV)
      Bandwidth ≤ 3 kHz
      Allowed in phone segments of HF bands.
    Fast-Scan Television (ATV)
      Bandwidth 6 MHz or greater.
      Restricted to 432 MHz band and above.

## Slide 24
G1B08 -- When choosing a transmitting frequency, what should you do to comply with good amateur practice?
A. Insure that the frequency and mode selected are within your license class privileges
B. Follow generally accepted band plans agreed to by the Amateur Radio community
C. Monitor the frequency before transmitting
D. All of these choices are correct

## Slide 25
G2A01 -- Which sideband is most commonly used for voice communications on frequencies of 14 MHz or higher?
A. Upper sideband
B. Lower sideband
C. Vestigial sideband
D. Double sideband

## Slide 26
G2A02 -- Which of the following modes is most commonly used for voice communications on the 160-meter, 75-meter, and 40-meter bands?
A. Upper sideband
B. Lower sideband
C. Vestigial sideband
D. Double sideband

## Slide 27
G2A03 -- Which of the following is most commonly used for SSB voice communications in the VHF and UHF bands?
A. Upper sideband
B. Lower sideband
C. Vestigial sideband
D. Double sideband

## Slide 28
G2A04 -- Which mode is most commonly used for voice communications on the 17-meter and 12-meter bands?
A. Upper sideband
B. Lower sideband
C. Vestigial sideband
D. Double sideband

## Slide 29
G2A05 -- Which mode of voice communication is most commonly used on the high frequency amateur bands?
A. Frequency modulation
B. Double sideband
C. Single sideband
D. Phase modulation

## Slide 30
G2A06 -- Which of the following is an advantage when using single sideband as compared to other analog voice modes on the HF amateur bands?
A. Very high fidelity voice modulation
B. Less bandwidth used and higher power efficiency
C. Ease of tuning on receive and immunity to impulse noise
D. Less subject to static crashes (atmospherics)

## Slide 31
G2A07 -- Which of the following statements is true of the single sideband voice mode?
A. Only one sideband and the carrier are transmitted; the other sideband is suppressed
B. Only one sideband is transmitted; the other sideband and carrier are suppressed
C. SSB is the only voice mode that is authorized on the 20-meter, 15-meter, and 10-meter amateur bands
D. SSB is the only mode that is authorized on the 160-meter, 75-meter and 40-meter amateur bands

## Slide 32
G2A08 -- Which of the following is a recommended way to break into a conversation when using phone?
A. Say "QRZ" several times followed by your call sign
B. Say your call sign during a break between transmissions from the other stations
C. Say "Break Break Break" and wait for a response
D. Say "CQ" followed by the call sign of either station

## Slide 33
G2A09 -- Why do most amateur stations use lower sideband on the 160-meter, 75-meter and 40-meter bands?
A. Lower sideband is more efficient than upper sideband at these frequencies
B. Lower sideband is the only sideband legal on these frequency bands
C. Because it is fully compatible with an AM detector
D. Current amateur practice is to use lower sideband on these frequency bands

## Slide 34
G2A11 -- What does the expression "CQ DX" usually indicate?
A. A general call for any station
B. The caller is listening for a station in Germany
C. The caller is looking for any station outside their own country
D. A distress call

## Slide 35
G2B01 -- Which of the following is true concerning access to frequencies in non-emergency situations?
A. Nets always have priority
B. QSO’s in process always have priority
C. Except during FCC declared emergencies, no one has priority access to frequencies
D. Contest operations must always yield to non-contest use of frequencies

## Slide 36
G2B03 -- If propagation changes during your contact and you notice increasing interference from other activity on the same frequency, what should you do?
A. Tell the interfering stations to change frequency
B. Report the interference to your local Amateur Auxiliary Coordinator
C. As a common courtesy, move your contact to another frequency
D. Increase power to overcome interference

## Slide 37
G2B04 -- When selecting a CW transmitting frequency, what minimum separation should be used to minimize interference to stations on adjacent frequencies?
A. 5 to 50 Hz
B. 150 to 500 Hz
C. 1 to 3 kHz
D. 3 to 6 kHz

## Slide 38
G2B05 -- What is the customary minimum frequency separation between SSB signals under normal conditions?
A. Between 150 and 500 Hz
B. Approximately 3 kHz
C. Approximately 6 kHz
D. Approximately 10 kHz

## Slide 39
G2B06 -- What is a practical way to avoid harmful interference on an apparently clear frequency before calling CQ on CW or phone?
A. Send "QRL?" on CW, followed by your call sign; or, if using phone, ask if the frequency is in use, followed by your call sign
B. Listen for 2 minutes before calling CQ
C. Send the letter "V" in Morse code several times and listen for a response or say "test" several times and listen for a response
D. Send “QSY” on CW or if using phone, announce “the frequency is in use”, then send your call and listen for a response

## Slide 40
G2B07 -- Which of the following complies with good amateur practice when choosing a frequency on which to initiate a call?
A. Check to see if the channel is assigned to another station
B. Identify your station by transmitting your call sign at least 3 times
C. Follow the voluntary band plan for the operating mode you intend to use
D. All of these choices are correct

## Slide 41
G2B08 -- What is the “DX window” in a voluntary band plan?
A. A portion of the band that should not be used for contacts between stations within the 48 contiguous United States
B. An FCC rule that prohibits contacts between stations within the United States and possessions in that portion of the band
C. An FCC rule that allows only digital contacts in that portion of the band
D. A portion of the band that has been voluntarily set aside for digital contacts only

## Slide 42
G2C04 -- What does the Q signal "QRL?" mean?
A. "Will you keep the frequency clear?"
B. "Are you operating full break-in" or "Can you operate full break-in?"
C. "Are you listening only for a specific station?"
D. "Are you busy?", or "Is this frequency in use?"

## Slide 43
G2D08 -- What is a reason why many amateurs keep a station log?
A. The ITU requires a log of all international contacts
B. The ITU requires a log of all international third party traffic
C. The log provides evidence of operation needed to renew a license without retest
D. To help with a reply if the FCC requests information

## Slide 44
G2D09 -- What information is traditionally contained in a station log?
A. Date and time of contact
B. Band and/or frequency of the contact
C. Call sign of station contacted and the signal report given
D. All of these choices are correct

## Slide 45
HF Operating Techniques
HF Receiving
  FM receivers normally only have volume, squelch, & frequency (channel) controls.
  SSB/CW receivers have MANY more controls to adjust operation.

## Slide 46
HF Receiving
  Selectivity
    Ability to reject strong signals close to the desired frequency.
    More important than sensitivity.
      Primary noise source is atmosphere rather than receiver circuitry.
HF Operating Techniques

## Slide 47
HF Receiving
  Receiver Incremental Tuning (RIT)
    Tunes receiver slightly off of transmit frequency.
  Transmitter Incremental Tuning (XIT)
    Tunes transmitter slightly off of receive frequency.
  Overload & Intermodulation
HF Operating Techniques

## Slide 48
HF Transmitting
  Phone
    VOX – Voice-operated transmit.
      Allows “hands-free” operation.
      3 Controls
        VOX Gain
        VOX Delay
        Anti-VOX
HF Operating Techniques

## Slide 49
HF Transmitting
  Phone Procedures & Abbreviations
    Prowords
    “Q” Signals
    No “10-Codes”
HF Operating Techniques

## Slide 50
HF Transmitting
  CW
    Straight Key
HF Operating Techniques

## Slide 51
HF Transmitting
  CW
    Semi-Automatic Key or “Bug”
HF Operating Techniques

## Slide 52
HF Transmitting
  CW
    Electronic Keyer
      Creates strings of “dits” & “dahs”.
      Built into most modern transceivers.
HF Operating Techniques

## Slide 53
HF Transmitting
  CW
      Single-Paddle Key
HF Operating Techniques

## Slide 54
HF Transmitting
  CW
      Dual-Paddle Key (Iambic)
HF Operating Techniques

## Slide 55
HF Transmitting
  CW
    Keyboard
HF Operating Techniques

## Slide 56
HF Transmitting
  CW
    T-R Switching
      MOX
      Semi Break-In (Semi QSK)
      Full Break-In (Full QSK)
HF Operating Techniques

## Slide 57
HF Transmitting
  CW & Digital Procedures & Abbreviations
    Abbreviations are used to shorten common words:
HF Operating Techniques

## Slide 58
HF Transmitting
  CW Procedures & Abbreviations
    Prosigns are used to organize/control communications:
HF Operating Techniques

## Slide 59
HF Transmitting
  CW Procedures & Abbreviations
    Q-Signals replace an entire sentence or phrase with a group of 3 letters.
      Originally developed for the commercial radiotelegraph service. (circa 1909)
      Add a “?” to change statement to a question.
HF Operating Techniques

## Slide 60
Q-Signal | Definition
QRL / QRL? | I am busy. / Are you busy? This frequency is in use. / Is this frequency in use?
QRM / QRM? | I have interference. / Do you have interference?
QRN / QRN? | I am troubled by static. / Are you troubled by static?
QRO / QRO? | Increase power. / Shall I increase power?
QRP / QRP? | Decrease power. / Shall I decrease power?
QRQ / QRQ? | Send faster. / Shall I send faster? (Can add speed in wpm)
QRS / QRS? | Send more slowly. Shall I send more slowly? (Can add speed in wpm)
QRT / QRT? | Stop sending. / Shall I stop sending?
QRV / QRV? | I am ready. / Are you ready?
HF Operating Techniques

## Slide 61
Q-Signal | Definition
QRX / QRX? | I will call you again at <time> on <freq>. Shall I call you again at <time> on <freq>? Also: Stand-By or Wait.
QRZ / QRZ? | <call> is calling you on <freq>. / Who is calling me?
QSB / QSB? | Your signals are fading. / Are my signals fading?
QSK / QSK? | I can hear you between my signals. Can you hear me between your signals?
QSL / QSL? | I am acknowledging receipt. / Can you acknowledge receipt?
QST | Here is a broadcast message for all amateurs.
QSY / QSY? | Change frequency. / Shall I change frequency? (Can add frequency or frequency offset.)
QTH / QTH? | My location is <location>. / What is your location?
HF Operating Techniques

## Slide 62
Signal Reports
  Readability, Strength, Tone (RST)
    Used to exchange information about the strength & quality of radio transmissions.
    In contests “cut” numbers are often used.
      A = 1
      N = 9
      T = 0
HF Operating Techniques

## Slide 63
Signal Reports
Readability | 
1 | Unreadable
2 | Barely readable, occasional words distinguishable
3 | Readable with considerable difficulty
4 | Readable with practically no difficulty
5 | Perfectly readable
HF Operating Techniques

## Slide 64
Signal Reports
  “S”-Meter on radio is an attempt to quantify signal strength readings.
  “S9” defined as 50μV signal at antenna terminals.
Strength | 
1 | Faint signal, barely perceptible
2 | Very weak
3 | Weak
4 | Fair
5 | Fairly good
6 | Good
7 | Strong
8 | Moderately strong
9 | Very strong signals
HF Operating Techniques

## Slide 65
Signal Reports
Tone | 
1 | 60Hz AC or less, very rough and broad
2 | Very rough AC, very harsh and broad
3 | Rough AC tone, rectified but not filtered
4 | Rough note, some trace of filtering
5 | Filtered rectified AC but strongly ripple-modulated
6 | Filtered tone, definite trace of ripple modulation
7 | Near pure tone, trace of ripple modulation
8 | Near perfect tone, slight trace of modulation
9 | Perfect tone, no trace of ripple or modulation of any kind
HF Operating Techniques

## Slide 66
Signal Reports
  Tone is omitted on phone.
  “C” at end indicates unstable tone or “chirp”.
  “K” at end indicates key clicks.
  “X” at end indicates exceptionally stable tone. (Not normally used any more.)
HF Operating Techniques

## Slide 67
G2A10 -- Which of the following statements is true of voice VOX operation versus PTT operation?
A. The received signal is more natural sounding
B. It allows "hands free" operation
C. It occupies less bandwidth
D. It provides more power output

## Slide 68
G2C01 -- Which of the following describes full break-in telegraphy (QSK)?
A. Breaking stations send the Morse code prosign BK
B. Automatic keyers are used to send Morse code instead of hand keys
C. An operator must activate a manual send/receive switch before and after every transmission
D. Transmitting stations can receive between code characters and elements

## Slide 69
G2C02 -- What should you do if a CW station sends "QRS"?
A. Send slower
B. Change frequency
C. Increase your power
D. Repeat everything twice

## Slide 70
G2C03 -- What does it mean when a CW operator sends "KN" at the end of a transmission?
A. Listening for novice stations
B. Operating full break-in
C. Listening only for a specific station or stations
D. Closing station now

## Slide 71
G2C05 -- What is the best speed to use answering a CQ in Morse Code?
A. The fastest speed at which you are comfortable copying
B. The speed at which the CQ was sent
C. A slow speed until contact is established
D. At the standard calling speed of 5 wpm

## Slide 72
G2C06 -- What does the term “zero beat” mean in CW operation?
A. Matching the speed of the transmitting station
B. Operating split to avoid interference on frequency
C. Sending without error
D. Matching your transmit frequency to the frequency of a received signal.

## Slide 73
G2C07 -- When sending CW, what does a “C” mean when added to the RST report?
A. Chirpy or unstable signal
B. Report was read from S meter reading rather than estimated
C. 100 percent copy
D. Key clicks

## Slide 74
G2C08 -- What prosign is sent to indicate the end of a formal message when using CW?
A. SK
B. BK
C. AR
D. KN

## Slide 75
G2C09 -- What does the Q signal "QSL" mean?
A. Send slower
B. We have already confirmed by card
C. I acknowledge receipt
D. We have worked before

## Slide 76
G2C10 -- What does the Q signal "QRN" mean?
A. Send more slowly
B. I am troubled by static
C. Zero beat my signal
D. Stop sending

## Slide 77
G2C11 -- What does the Q signal “QRV” mean?
A. You are sending too fast
B. There is interference on the frequency
C. I am quitting for the day
D. I am ready to receive messages

## Slide 78
G4A10 -- What is the purpose of an electronic keyer?
A. Automatic transmit/receive switching
B. Automatic generation of strings of dots and dashes for CW operation
C. VOX operation
D. Computer interface for PSK and RTTY operation

## Slide 79
Emergency Operation
Emergency operations are one of the basic purposes of the Amateur Radio Service.
The ability to assist with emergencies is the primary reason that many individuals get their license.
All amateurs should be prepared to respond properly if an emergency arises.

## Slide 80
  Can provide communications for broadcasters only if:
    Necessary to save lives or protect property.
    No other means of communications available.
Emergency Operation

## Slide 81
ARES & RACES
Emergency Operation

## Slide 82
Amateur Radio Emergency Service (ARES)
  Part of ARRL field organization.
  Open to any amateur radio operator regardless of ARRL membership.
  No official recognition in FCC rules.
Emergency Operation

## Slide 83
Radio Amateur Civil Emergency Service (RACES)
  Part of FEMA/SEMA/EMA.
  Established by FCC Rules & Regulations (§97.407).
  President's War Emergency Powers.
Emergency Operation

## Slide 84
Distress Calls
  Responding to a Distress Call.
    Make certain that you are the station who can best handle the traffic.
    Immediately acknowledge calling station.
    Accurately copy information.
    Notify proper authorities.
    Stay in contact with calling station until help arrives.
Emergency Operation

## Slide 85
Distress Calls
  Placing a Distress Call.
    Send the distress call proword or prosign 3 times.
      Phone proword = MAYDAY
      CW Prosign = SOS
    Send your callsign 3 times.
      On phone, use the ICAO phonetic alphabet.
    Send the location & nature of the emergency.
    End with the appropriate proword or prosign.
      Phone proword = Over
      CW prosign = K
Emergency Operation

## Slide 86
Distress Calls
  Placing a Distress Call.
    During the existence of the emergency, you may use ANY frequency available without regard to radio service or license class.
    During the existence of the emergency, you may contact ANY station without regard to radio service.
Emergency Operation

## Slide 87
Distress Calls
  Do what is necessary to accomplish communication & ask forgiveness later.
    ANY frequency (not just amateur).
    Contact ANY station (not just amateur).
Emergency Operation

## Slide 88
G1B04 -- Which of the following must be true before amateur stations may provide communications to broadcasters for dissemination to the public?
A. The communications must directly relate to the immediate safety of human life or protection of property and there must be no other means of communication reasonably available before or at the time of the event
B. The communications must be approved by a local emergency preparedness official and conducted on officially designated frequencies
C. The FCC must have declared a state of emergency
D. All of these choices are correct

## Slide 89
G2B02 -- What is the first thing you should do if you are communicating with another amateur station and hear a station in distress break in?
A. Continue your communication because you were on frequency first
B. Acknowledge the station in distress and determine what assistance may be needed
C. Change to a different frequency
D. Immediately cease all transmissions

## Slide 90
G2B09 -- Who may be the control operator of an amateur station transmitting in RACES to assist relief operations during a disaster?
A. Only a person holding an FCC issued amateur operator license
B. Only a RACES net control operator
C. A person holding an FCC issued amateur operator license or an appropriate government official
D. Any control operator when normal communication systems are operational

## Slide 91
G2B10 -- When may the FCC restrict normal frequency operations of amateur stations participating in RACES?
A. When they declare a temporary state of communication emergency
B. When they seize your equipment for use in disaster communications
C. Only when all amateur stations are instructed to stop transmitting
D. When the President’s War Emergency Powers have been invoked

## Slide 92
G2B11 -- What frequency should be used to send a distress call?
A. Whatever frequency has the best chance of communicating the distress message
B. Only frequencies authorized for RACES or ARES stations
C. Only frequencies that are within your operating privileges
D. Only frequencies used by police, fire or emergency medical services

## Slide 93
G2B12 -- When is an amateur station allowed to use any means at its disposal to assist another station in distress?
A. Only when transmitting in RACES
B. At any time when transmitting in an organized net
C. At any time during an actual emergency
D. Only on authorized HF frequencies